## Slide 1: Socket Programming Project: IP Network Emulation
Jaehoon (Paul) Jeong
pauljeong@skku.edu

## Slide 2: Project Objectives
To Understand the IP Networking
  IP Addressing
    IP Address Classification
    IP Subnetting by Network Masking
  IP Routing Protocol
    Distance Vector Routing Protocol (e.g., RIP)
  IP Packet Forwarding
  Address Resolution Protocol (ARP)
  Domain Name Service (DNS)

## Slide 3: IP Packet Routing
IP Packet
IP Packet
The shortest path between Host 1 and Host 2: <Host 1, Router 1, Router 2, Router 3, Host 2>

## Slide 4: Packet Formation in the Protocol Stacks
Application Layer
IP Layer
Ethernet Layer
Simplified Protocol Stacks
Application Data
Application Data
IP Header
Application Data
IP Header
Ethernet Header
Encapsulation
Decapsulation

## Slide 5: Packet Transmission Procedure in the IP Host
DNS Resolution
  Resolve the host DNS name into the corresponding IP address by DNS Resolver.
Decision of Next Hop
  If the destination IP address has the same network address as its own one, then
    Decide the MAC address of the destination host by ARP.
  Otherwise,
    Decide the MAC address of the default router by ARP.
Transmission of the Ethernet Frame
  Send the Ethernet Frame including IP Packet.

## Slide 6: Routing Decision in the IP Router
Receiving an IP Packet
If the IP Packet is the routing info, then
  Update the routing table and forwarding table.
  Send the updated routing information to its neighbors
Otherwise,
  Forward the IP Packet to the appropriate next hop with its forwarding table.
    The appropriate MAC address of the next hop is determined by ARP.

## Slide 7: Distance Vector Routing Protocol (DV)
DV is based on Bellman and Ford’s shortest path algorithm.
The difference
  Bellman and Ford’s algorithm is performed with the complete network topology.
  DV is performed with the partial network topology and is continuously updated with the neighbors’ routing information.

## Slide 8: Template Codes
Files
  README explains the files and how to compile and run the programs
  host.c contains source code of host program
  hub.c contains source code of hub program
  router.c contains source code of router program
  utils.c utilities used by all the programs
  common.h common macros and function prototypes
  dist-vec.h header file for distance vector routing protocol
  dist-vec.c functions for handling distance vector routing protocol
  Makefile.template template file for generating a Makefile with 'Configure' shell script according to the operating system, such as Linux and SunOS
  host host executable in Linux
  hub hub executable in Linux
  router router executable in Linux
  ip-addr.conf configuration file for the IP address assignment for hubs, routers, and hosts
  mac-addr.conf configuration file for the MAC address assignment for routers and hosts
  gateway.conf configuration file for configuring default gateway at hosts

## Slide 9: Network Topology constructed by the configuration files

## Slide 10: ip-addr.conf

## Slide 11: gateway.conf

## Slide 12: mac-addr.conf

## Slide 13: Testing Scenarios
Single LAN Scenario
Two LANs Scenario
Multiple LANs Scenario

## Slide 14: Single LAN Scenario

## Slide 15: Two LANs Scenario

## Slide 16: Multiple LANs Scenario (1/2)

## Slide 17: Multiple LANs Scenario (2/2)

## Slide 18: Grading Policy
1. Design document (20%)
2. Routing table exchange through DV routing protocol (20%)
3. Establishment of a routing table in each router (10%)
4. Establishment of a forwarding table in each router (10%)
5. Routing of IP packet from a source host to a destination host (10%)
6. Dynamic update of routing tables in routers by the router insertion and deletion (15%)
7. Detection and advertisement of link breakage (15%)